## Slide 1
Fleet Maintenance Prioritization
Evaluating Dispatcher Priorities Against Operational Impact in Municipal Fleet Operations
CORE BUSINESS PROBLEM
Fleet maintenance dispatchers ration limited shop capacity using a coarse priority signal. When 98%+ of work orders share the exact same priority code, genuinely high-impact jobs hide in the queue—driving avoidable downtime and excess costs.
GROUP A1 PROJECT TEAM & DATASET
Data Source: City of Cincinnati Open Data Portal (332,372 Work Orders • 8,353 Equipment Units)

## Slide 2
Problem: 98.31% of all work orders sit under Priority Code 3.
Why it Matters: A single dominant category renders the priority field virtually useless for day-to-day shop sequencing, creating queue bottlenecks.
Problem: Maintenance cost and vehicle downtime are nearly uncorrelated (r = 0.086).
Why it Matters: Standard triage focuses on expensive repairs, completely missing lower-cost jobs that cause massive operational downtime.
Problem: ANOVA shows statistically significant code differences but tiny effect sizes (η² ≈ 0.002).
Why it Matters: Assigned priority codes explain less than 0.25% of the real variation in cost or downtime.
Problem: 98.7% of high-cost, labor-intensive jobs remain hidden under standard Code 3.
Why it Matters: Critical jobs receive routine scheduling, causing delayed shop throughput and unmitigated fleet risk.
1. Priority Code Congestion
2. Operational Impact Blind Spots
3. Negligible Practical Differentiation
4. Hidden High-Risk Work Orders
Coarse Triage & Priority Congestion Impair Fleet Operations

## Slide 3
Identified Problem | Analytical Model / Activity | What It Helps Answer & Solve
Code Congestion 98.31% orders in Code 3 | Priority Distribution EDA & Chi-Square | Establishes the empirical baseline of dispatcher coding concentration and demonstrates extreme category skew.
Impact Blind Spots Cost vs. downtime mismatch | Pareto & Dual-Threshold Feature Design | Defines a composite HIGH_IMPACT metric (top 15% cost or downtime) to capture total operational disruption.
Ineffective Triage Current codes lack signal | One-Way ANOVA & Effect Size (η²) | Proves that despite p < 0.001, priority code explains < 0.25% variance, justifying an analytical screening layer.
Hidden Operational Profiles Unseen resource heavy jobs | K-Means Clustering (K=4) | Uncovers 4 distinct operational profiles (including labor-heavy jobs) buried inside standard priority codes.
Early Triage Deficit Need early risk warning | MLR & Logistic Risk Classifier | Quantifies early cost drivers and provides an actionable risk screening model achieving 70.6% recall.
Mapping Core Business Problems to Analytical Methods

## Slide 4
332,372
CLEANED OBSERVATIONS
From 332,420 raw records
8,353
EQUIPMENT UNITS
Across municipal departments
37
RAW VARIABLES
Costs, hours, job types, dates
25.31%
HIGH-IMPACT TARGET
84,123 flagged work orders
Primary Data Source & Context
Primary Operational Target Variable
HIGH_IMPACT (Engineered Binary Target):
Calculated as exceeding the 85th percentile threshold on either cost or total vehicle downtime.
Source: City of Cincinnati Open Data Portal (Dataset ID: 2a8x-bxjm).
Scope: Complete fleet preventative maintenance & repair records.
Core Job Types: Preventative Maintenance (PM) vs. Unplanned REPAIR.
Triage Mechanism: PRI_PRIORITY_CODE (dispatcher assigned 1 to 4).
Dataset Overview: 332,372 Cleaned Work Orders

## Slide 5
Variable Name | Technical & Operational Meaning | Business Relevance & Risk Context
TOTAL_COST | Sum of labor cost, parts cost, and commercial cost per work order. | Direct financial maintenance burden on the municipal budget.
TOTAL_DOWNTIME_HOURS | Combined total of user downtime and shop repair downtime. | Measures vehicle availability and operational disruption to public services.
PRI_PRIORITY_CODE | Dispatcher-assigned urgency code ranging from 1 (Highest) to 4 (Lowest). | Current operational triage signal being evaluated for effectiveness.
JOB_TYPE | Categorical indicator of work scope: PM (Preventative) vs. REPAIR. | Strong early indicator of expected cost, labor hours, and failure severity.
EQUIP_PRIOR_AVG_COST | Historical average maintenance cost for the specific equipment unit. | Forward-looking equipment risk signal capturing aging asset health.
DEPT_AVG_COST | Train-only encoded department-level average maintenance cost. | Captures operational intensity differences across departments (e.g., Police vs Parks).
Core Features Balance Financial & Operational Risk

## Slide 6
Methodological Rigor: All modeling excludes post-repair variables (e.g., labor hours) known only after work completion, ensuring predictive models solve real early-prioritization challenges.
Data Collection
332K+ Open Data Records
Cleaning
Remove 48 Invalid Rows
EDA & Pareto
Cost & Downtime Distributions
Feature Eng.
Prior History (No Leakage)
Stat Testing
ANOVA & Effect Size (η²)
Modeling
K-Means / MLR / Logistic
Diagnostics
VIF, HC3, ROC Thresholds
Recommendations
Risk Screening Layer
Eight-Stage Analytical Framework Ensures Rigorous Output

## Slide 7
Leakage Control Safeguard
Predictive models explicitly exclude LABOR_HOURS, PARTS_COST, and direct components of total cost. Including them would re-derive the target rather than answer the real managerial question: Can we screen risk early at work order creation?
1. Cleaning & Outlier Handling
2. Feature Engineering & History
Negative Value Removal: 48 records with negative cost or labor hours were removed as invalid.
Sparse Column Removal: Column REF_WORK_ORDER_NO dropped due to ~99.9% missing values.
No Row Duplicates: Zero exact duplicate work-order rows found in dataset.
Equipment History: Derived EQUIP_PRIOR_WO_COUNT and EQUIP_PRIOR_AVG_COST strictly from prior chronological work orders.
Combined Downtime: Aggregated user downtime and shop downtime into TOTAL_DOWNTIME_HOURS.
Department Encoding: Target-encoded using training split only to avoid data leakage.
Data Preparation & Strict Leakage Control

## Slide 8
Business Takeaway
r = 0.086
PEARSON CORRELATION COEFFICIENT
The correlation between Total Cost and Total Downtime is virtually zero. Expensive jobs are not necessarily the same jobs that disrupt equipment availability.
Dual Impact Nature: Operational disruption occurs in two distinct ways—high financial cost or severe vehicle unavailability.
Cost-Only Flaw: A priority system focused purely on repair cost would miss low-cost jobs that lock up vital public service vehicles for hundreds of hours.
Dual Target Required: Triage must evaluate cost and downtime as complementary risk dimensions.
$563.82
MEAN COST
Median: $182.62
388.52 hrs
MEAN DOWNTIME
Median: 34.56 hrs
Cost & Downtime Are Independent Operational Burdens

## Slide 9
19.1%
FLEET ASSET CONCENTRATION
Pareto analysis reveals that just 1,595 equipment units out of 8,353 generate 80% of total maintenance expenditure.
Strategic Implications for Fleet Managers
Job Type Structural Signal:
Unplanned REPAIR work orders average $670.44—more than 3x the cost of Preventative Maintenance (PM) at $213.34.
Equipment Watchlist: Chronic high-cost equipment units can be tracked on an automated watchlist for proactive intervention.
Early Job Type Signal: JOB_TYPE is known at work order intake and serves as an immediate structural indicator of risk.
Targeted Maintenance: Focusing predictive screening on high-frequency, high-cost assets provides maximum financial leverage.
19.1% of Equipment Units Drive 80% of Maintenance Cost

## Slide 10
Key Takeaway from Target Composition
Only 18.5% of high-impact work orders exceed both the cost and downtime 85th percentile cutoffs simultaneously. This confirms that maintenance cost and downtime capture fundamentally different dimensions of operational burden. Combining them into HIGH_IMPACT ensures comprehensive risk screening.
34,162
HIGH COST ONLY
Cost > $771.77
34,163
HIGH DOWNTIME ONLY
Downtime > 475.25 hrs
15,798
BOTH THRESHOLDS
High Cost & Downtime
Dual-Threshold Rule Identifies 25.31% High-Impact Cases

## Slide 11
Analytical Purpose
Determine whether existing priority codes and job types reflect real differences in realized operational outcomes.
Diagnostic Metrics & Formulas
Eta-Squared (η²) Effect Size Formula:
Interpretation Scale: η² ≈ 0.01 (Small), η² ≈ 0.06 (Medium), η² ≈ 0.14 (Large). Tests whether statistical significance translates into managerial utility.
One-Way ANOVA: Tests mean differences in cost and downtime across PRI_PRIORITY_CODE (1–4).
Effect Size (η²): Evaluates practical magnitude of priority code differentiation.
Two-Sample T-Test: Compares labor hours and duration across high-impact vs normal jobs.
Chi-Square Test: Assesses association between JOB_TYPE and HIGH_IMPACT.
Technique 1: Statistical Testing (ANOVA & T-Tests)

## Slide 12
Outcome Variable | ANOVA F-Statistic | p-value | Eta-Squared (η²) Effect Size | Practical Meaning
TOTAL_COST | 152.57 | 8.15 × 10⁻⁹⁹ | 0.0014 (0.14%) | Negligible practical impact
TOTAL_DOWNTIME_HOURS | 250.90 | 1.20 × 10⁻¹⁶² | 0.0023 (0.23%) | Negligible practical impact
98.31%
PRIORITY CODE 3 CONCENTRATION
Code 1: 0.82% • Code 2: 0.53% • Code 4: 0.34%
Business Takeaway
With 332K+ records, even microscopic differences produce extreme p-values. However, effect sizes (η² < 0.25%) prove priority codes explain almost no real variance in cost or downtime. The priority system fails to differentiate work orders in practice.
Priority Codes Offer Virtually Zero Practical Differentiation

## Slide 13
Analytical Purpose
Discover hidden operational work-order profiles using unsupervised segmentation, independent of dispatcher priority codes.
Cluster Optimization & Scaling
Features scaled using Min-Max Normalization:
Ensures high-magnitude features (downtime hours) do not dominate smaller features (labor hours) during distance calculations.
Feature Inputs: Min-Max scaled Total Cost, Total Downtime, Labor Hours, Duration, and Delay.
Cluster Optimization: K = 4 selected via Elbow Method optimization.
Objective: Test whether distinct operational profiles exist within the dominant Priority Code 3.
Technique 2: Unsupervised K-Means Clustering

## Slide 14
Cluster ID & Profile | Work Orders | Avg Total Cost | Avg Downtime | Priority Code 3 Share
Cluster 0: Routine / Low Burden | 31,164 | $172.00 | 172 hrs | 98.1%
Cluster 1: Downtime-Heavy | 3,579 | $164.00 | 710 hrs | 98.4%
Cluster 2: High-Cost / Labor-Intensive | 1,760 | $1,262.00 | 453 hrs | 98.7%
Cluster 3: Scheduling-Delay Dominated | 577 | $823.00 | 18 hrs | 97.9%
Key Segmentation Insight
98.7% of Cluster 2 (the most expensive, labor-intensive work orders) is trapped inside Priority Code 3. Unsupervised segmentation proves from an independent angle that dispatcher priority codes fail to separate heavy maintenance from routine jobs.
Unsupervised Clusters Expose Trapped High-Burden Jobs

## Slide 15
Analytical Purpose
Quantify directional cost drivers using information available strictly at work order intake.
Variance Inflation Factor (VIF) Diagnostic
Max VIF dropped from 16.50 to 5.85 after removing collinear features, ensuring stable coefficient estimation.
Predictors: Priority Code, Job Type, Equipment Prior Cost, Prior WO Count, Dept Average Cost.
Multicollinearity Check: Evaluated using Variance Inflation Factor (VIF).
Heteroscedasticity Adjustment: Applied HC3 robust standard errors following Breusch-Pagan test.
Technique 3: Multiple Linear Regression (MLR)

## Slide 16
Predictor Variable | MLR Coefficient | p-value | Business Interpretation
PRI_PRIORITY_CODE | +$195.45 | < 0.001 | Higher numeric priority step associates with higher expected cost.
JOB_TYPE_REPAIR | +$293.31 | < 0.001 | Unplanned repairs add $293.31 vs baseline PM work orders.
EQUIP_PRIOR_AVG_COST | +$0.315 / $1 | < 0.001 | Historical asset cost carries forward-looking risk signal.
EQUIP_PRIOR_WO_COUNT | +$1.458 / WO | < 0.001 | Frequent maintenance history increases current job cost.
R² = 0.0725
MODEL EXPLANATORY POWER
Test Set Performance
Managerial Takeaway
Early intake variables are statistically significant directional indicators, but explain only 7.25% of total cost variance. MLR serves to identify risk factors, not precise budget forecasting.
Intake Variables Provide Directional Cost Signals

## Slide 17
Classification Cutoff | Recall (High Impact) | Precision | Share Flagged for Review | Operational Assessment
Standard Cutoff (0.50) | 1.10% | 49.86% | Very Small (< 1%) | Unusable: Misses 98.9% of high-impact risks due to class imbalance.
Recommended Cutoff (0.25) | 70.59% | 31.62% | 55.40% | Effective Screening: Captures 70.6% of risks for advisory review.
0.641
ROC-AUC SCORE
Modest, useful early screening discrimination
70.59%
HIGH-IMPACT RECALL @ 0.25 CUTOFF
Flags 55.4% of orders for manager review
Logistic Classifier Achieves 70.6% Recall at 0.25 Cutoff

## Slide 18
1. Cost & Downtime are Distinct (r = 0.086): Dual-dimension targeting is essential; cost alone misses fleet disruption.
2. Code Congestion (98.31% in Code 3): Existing priority system provides near-zero routine differentiation.
3. Low Practical Effect (η² ≈ 0.002): Statistical significance in large samples does not mean useful shop triage.
4. Hidden High-Risk Profiles (K-Means): 98.7% of high-cost, labor-intensive jobs are trapped in standard Priority 3.
5. Repair Jobs Carry High Risk (Odds Ratio 2.96): Unplanned repair classification is a vital early intake risk signal.
6. Early Cost Prediction is Inherently Noisy (R² = 0.0725): Models indicate directional risk context rather than exact budget figures.
7. Feasible Risk Screening (70.6% Recall): A 0.25 logistic cutoff successfully surfaces high-impact work orders for review.
Seven Core Insights Synthesize Analytical Findings

## Slide 19
Original Problem | Evidence from Analysis | Data-Driven Solution
Priority Code Congestion | 98.31% of work orders sit in Priority Code 3. | Layer data-driven risk screening inside Priority Code 3 to differentiate jobs.
Operational Impact Blind Spots | Cost & downtime correlate at r = 0.086. | Implement dual-threshold HIGH_IMPACT rule combining cost and downtime.
Negligible Code Value | ANOVA effect sizes η² < 0.0025. | Supplement manual codes with automated predictive risk scores.
Hidden Resource Heavy Jobs | Cluster 2 ($1,262 avg cost) is 98.7% Code 3. | Flag high-cost, high-labor repair work orders at creation for managerial review.
Analytics Directly Solves Identified Triage Problems

## Slide 20
1. Equipment Risk Watchlist
Track the 19.1% of fleet units driving 80% of costs for proactive replacement and maintenance.
2. Data-Assisted Screening
Display predictive risk scores alongside dispatcher priority codes at work order intake.
3. Target Priority Code 3
Focus analytics specifically within Code 3, where 98.31% of queue differentiation is needed.
4. Capacity-Calibrated Thresholds
Set operational cutoff (e.g., 0.25) based on available shop manager review capacity.
5. Pilot Advisory Deployment
Introduce risk flags as decision support before automating any priority changes.
Five Strategic Recommendations for Fleet Management

## Slide 21
Phase 1: Short-Term
MONTHS 1 – 3
Phase 2: Medium-Term
MONTHS 3 – 6
Phase 3: Long-Term
MONTHS 6 – 12
Establish equipment risk watchlist.
Validate 85th percentile threshold with fleet managers.
Finalize intake data feature pipeline.
Deploy Priority Code 3 risk screening layer.
Calibrate decision cutoff (0.25) to shop review load.
Train dispatchers on advisory risk scores.
Integrate risk scoring into CMMS / ERP dashboard.
Monitor manager adoption & shop throughput.
Refine models with real-time feedback.
Phased Implementation Roadmap Ensures Controlled Adoption

## Slide 22
Analytical & Data Limitations
Future Research & Enhancement
Threshold Validation: 85th percentile cutoff is analytical and requires formal operational validation by fleet managers.
Observational Data: Relationships reflect statistical associations, not established causal effects.
Unexplained Variance: MLR R² of 0.0725 highlights high intrinsic cost noise at work order intake.
Review Capacity Load: 0.25 logistic cutoff flags 55.4% of orders, requiring managed review workflows.
Vehicle Criticality: Incorporate department service-level agreements (SLAs) and vehicle operational mission criticality.
Shop Capacity Tracking: Integrate real-time bay availability and technician specialty scheduling queues.
Dynamic Thresholding: Automate decision cutoffs based on daily shop queue lengths and backlog volume.
Practical Limitations Frame Future Scope

## Slide 23
Executive Conclusion: Data-Assisted Fleet Triage
"Analytics should not replace dispatcher judgment—it should illuminate hidden risk within standard priority queues."
1. WHAT DID WE FIND?
98.31% of work orders sit in Priority Code 3, trapping 98.7% of high-cost, labor-intensive jobs without triage differentiation.
2. WHY DOES IT MATTER?
Current priority codes explain under 0.25% of variance (η² ≈ 0.002), causing high-impact jobs to sit in queues and driving avoidable downtime.
3. WHAT SHOULD BE DONE?
Layer an advisory risk-screening model inside Priority Code 3 using job type and equipment history to recall 70.6% of high-impact risks.